## Slide 1: Start the program
Double Click

## Slide 2: Start Labview
Single Click

## Slide 3: Load Mask
1. Click Arrow
Select Mask
Load Mask
Mask Appears and Grid populates

## Slide 4: Name Data
Fill in information needed to uniquely identify the dataset

## Slide 5: Custom Paths
Click pads to deselect/select
Click twice to name junction

## Slide 6: Align 1
Use Physical Joy stick
Or Virtual Joy stick
To move left needle to location circled on mask
Move needle to contact
Then mark position

## Slide 7: Align 2
1. Click Move to position 2 to get auto align
2. Align left needle with selected pad
3. Use joystick to touch needle to pad
Set the position

## Slide 8: Align 3
1. Click Move to position 2 to get auto align
2. Align left needle with selected pad
3. Use joystick to touch needle to pad
Set the position

## Slide 9: Align 2
1. Click Move to position 3 to get auto align
2. Align left needle with selected pad
3. Use joystick to touch needle to pad
Set the position

## Slide 10: Run Program
Return to Position 1
Run Program
Check to make sure no errors appear and Keithley is happy

## Slide 11: Data AutoSave
Data is saved to C:\Data for analysis ( accessible as \\biod1792\data from other computers)

## Slide 12: Mask Creation
Add dxf file to %%desktop\Automation\Waferplans\DXFFiles

## Slide 13: Create Wafer Definition
Use text editor (notepad) to open C:\Users\User\Desktop\Automation\WaferPlans\NewInstall_CopyAndChange.json
Change Replace to name of dxf file (no .dxf)
Save with same name as dxf file (.json extension)

## Slide 14: Load new plan
1. Restart program. (Close and hit red X)
2. Load new dxf file
3. Select Active dxf layer
Click on measure pad (left needle only)

## Slide 15: Name Junctions
Name Junctions for files
Save Mask when finished